## Slide 1: Optimal Resource Allocation in MU-MIMO Systems with Soft Video Delivery
Ticao Zhang and Shiwen Mao
School of Electrical and Computer Engineering
Auburn University
Auburn, AL 36849-5201
A proposal to the FiWIN IAB

## Slide 2: Problems to Solve and Industrial Relevance
Demand for wireless video
  78% of the world’s mobile data traffic will be video related by 2021
  Video call, IPTV, video conference, video live streaming are boosting
  Efficient and robust wireless video transmission technology
Conventional video coding (MPEG-4 over 802.11)
  Shannon’s source-channel separation theorem
    Source coding: represent video with the minimum number of bits (prediction, transformation, quantization and entropy coding)
    Channel coding: correct errors (reliable transmission)
  Drawback
    Lack of flexibility in handling channel and user heterogeneity
    Suffers from cliff-effect
  Reasons
    The sensitivity of entropy coding to bit errors
    In low SNR regime, error correction coding breakdown
    Quantization distortion cannot be recovered
    The bitrate for video broadcast/multicast cannot fit all receivers at the same time
Cisco visual networking index: Global mobile data trafﬁc forecast update, 2016–2021 white paper.

## Slide 3: Problems to Solve and Industrial Relevance
Layered scalable video coding (SVC)
  Separate channel and source coding + local buffer
    Encoder adjusts the source coding rate according to the buffer size
    Transmitter chooses the most appropriate modulation rate to send the packet out
  Drawback
    The efficiency of adaptive modulation and coding (AMC) relies on the timeliness and precision of channel feedback
    A difficult engineering tradeoff between the channel adaptation capability and the amount of induced delay
    Still suffers from the cliff-effect
Soft video transmission (SoftCast)
  Conventional design suffers severe cliff effect
  Layered video makes the cliff milder but introduced overhead and reduces the maximum video quality
  SoftCast video quality scales with the channel quality
Jakubczak, S., & Katabi, D. (2011). Softcast: one-size-fits-all wireless video. ACM SIGCOMM Computer Communication Review, 41(4), 449-450.
cliff effect

## Slide 4: Problems to Solve and Industrial Relevance
Soft video transmission (SoftCast)
  Features
    Joint channel and source coding
    Skips quantization and entropy coding
    Transmit power scaled discrete cosine transform (DCT) coefficients
    Amplitude modulation to minimize the end-to-end distortion
    All operations involved are linear
  Users gracefully improve video quality matching to their wireless channel quality
  Comparison
    Modulation
    Framework
Conventional video transmission
SoftCast
Conventional video transmission
SoftCast
Modulation comparison
R. Xiong, J. Zhang, F. Wu, J. Xu, and W. Gao, “Power distortion optimization for uncoded linear transformed transmission of images and videos,” IEEE Trans. Image Process., vol. 26, no. 1, pp. 222–236, Jan. 2017.

## Slide 5: Problems to Solve and Industrial Relevance
Soft video transmission (SoftCast)
  System Model
  Linear decoder
  Optimal power allocation
  Solution
  Challenges
    signal energy distribution (SED) needs to be well handled and exploited by the sender and receiver
    The overhead of metadata should be reduced
    A cross-layer joint resource optimization
    Incorporate the current soft video delivery system to a MU-MIMO system
    Hybrid digital and analog modulation
    …
is the power of each transmitted coefficient

## Slide 6: Existing Solutions and Their Limitations
Accurate signal energy distribution modeling
  Limitation
    Softcast: performance depends on chunk size, large metadata overhead
    L-shape modeling: simple but there is still large metadata overhead
    Gaussian Markov Random Field (GMRF) modeling: complex and not accurate enough
(a) the original video sequence (b) the corresponding DCT coefficients (c) the corresponding power (d) the corresponding power scaling coefficients
(a) the original video sequence (b) the corresponding DCT coefficients (c) the corresponding power (d) the corresponding power scaling coefficients
(a) Signal empirical distributions (SED)
for picture Lena, gray (b) SoftCast (c) L-shape modeling (d) GMRF modeling
[1] T. Fujihashi, T. Koike-Akino, T. Watanabe, and P. V. Orlik, “High-quality soft video delivery with GMRF-based overhead reduction,” IEEE Trans. Multimedia, vol. 20, no. 2, pp. 473–483, Feb. 2018.
[2] R. Xiong, J. Zhang, F. Wu, J. Xu, and W. Gao, “Power distortion optimization for uncoded linear transformed transmission of images and videos,” IEEE Trans. Image Process., vol. 26, no. 1, pp. 222–236, Jan. 2017.
DCT
DCT coefficients into chunks

## Slide 7: Existing Solutions and Their Limitations
Joint power and bandwidth allocation
  A large redundancy in the DCT coefficient
  Power and bandwidth tradeoff
    Cost-distortion optimization solution (heuristic)
    Resource allocation algorithm design
  Limitation
    Only works in single-input single-output (SISO) channel
    A cross-layer joint optimization is needed
(a) the original video sequence (b) the corresponding DCT coefficients (c) the corresponding power (d) the corresponding power scaling coefficients
D. Liu, J. Wu, H. Cui, D. Zhang, C. Luo, and F. Wu, “Cost-distortion optimization and resource control in pseudo-analog visual communications,” IEEE Trans. Multimedia, 2018.
Redundancy in DCT coefficients
Power and bandwidth tradeoff

## Slide 8: Proposed Solution and Its Benefits
Proposed solution
  Blind signal detection
    Scales each coefficient with an optimal scaling factor at the encoder
    Recover the video signal from the amplitude of the square of the received signal at the decoder
    Theoretical PSNR performance
  is the signal-to-noise ratio
  A cross layer joint bandwidth and power allocation
    Theoretical PSNR performance
    Geometric programming
  Benefits
    Metadata-free
    Theoretical results provide accurate prediction
    Improved PSNR performance
    Better optimization algorithm
is the signal to noise ratio

## Slide 9: Preliminary results
Outperforms SoftCast by approximately 2dB
Metadata-free
No SED modeling process
A trade-off between power allocation and bandwidth usage
Simulation results
  Proposed blind detection method
  Power and bandwidth tradeoff

## Slide 10: Challenges and Risks
Problems | Solutions
An extension to MIMO-OFDM | SVD channel decomposition Parallel SISO channels
Joint MU-MIMO resource allocation | Geometric optimization The derived theoretical results provide accurate prediction Low cost and efficient algorithms
Accurate SED modeling | Fit the SED plane with Gaussian process Fit the SED plane with deep learning
Testbed implementation | USRP Low complexity implementation 360o/HD video transmission Virtual reality extension

## Slide 11: Outcomes for Project Evaluations
Expected Benefits | Current Solution | Our Proposed Solutions
Improved PSNR performance | Chunk division | Blind detection that skips chunk division
Reduced bandwidth usage | Discard the least important chunks | Power reallocation with the aid of the derived theoretical results
Joint bandwidth and power optimization | A heuristic optimization/SISO channel | SVD channel decomposition + A cross layer joint optimization
An extension to MU-MIMO | Not supported | 

## Slide 12: Schedule and Tasks
Budget: (1 year) $25,000
Manpower: 1 GRA
Tasks | Schedule |  |  | 
 | H1 | H2 | H3 | H4
Investigation of an accurate signal detection algorithm with reduced metadata |  |  |  | 
Investigation of the theoretical performance for power-distortion optimization |  |  |  | 
Investigation of power and bandwidth usage tradeoff in a SISO soft video delivery system |  |  |  | 
Investigation of joint power and bandwidth allocation in an MU-MIMO soft video delivery system |  |  |  | 

## Slide 13: Thank You! Email: smao@ieee.org